## Slide 1
Jal Jeevan Mission under Ministry of Jal Shakti
Collectors' Peyjal Samvad
FROM GRASSROOTS TO FOREFRONT
District Water and Sanitation Mission(DWSM) ASR District , Andhra Pradesh
Presented By:
Shri AS DINESH KUMAR, I.A.S
Collector & District Magistrate,
Alluri Sitharama Raju District
Andhra Pradesh

## Slide 2: Glance of ASR District
Chart: No of Sources Availiable
| Spring Sources | Ground Water Sources | No of Reservoirs
No of Sources existing | 2223 | 5319 | 3
No of Sources currently working | 2223 | 5319 | 3
ASR should be a priority district because providing drinking water here is much harder than in normal areas
Due to very hilly terrain the expenditure for the establishment is 40% is higher than other districts.
Unreliable groundwater (seasonal changes around 50% ) and remote tribal villages (30% of villages reachable only by foot).
Geomorphology of the land is very fragile for borewell construction in the district.
Expected operations and Maintenance cost is approximately 19% of total Capital Cost.
Chart: 
| No of habitations covered | No of habitations works completed | No of habitations works to be completed | % of works completed
JJM | 4625 | 1847 | 2778 | 0.39935
As of now in ASR district completed around 7,000 JJM works and nearly 1.8 lakh household tap connections showing strong progress

## Slide 3
Unique Challenges in the ASR District
Geographical
Your Title 02
Material transport and work execution are difficult due to remote foot-access-only tribal habitations in hilly terrain.
Irregular or absent power supply limits feasibility of conventional pumping-based drinking water systems.
Shortage of skilled manpower and contractors delays execution, O&M and ensures higher dependency on external technical support.
Institutional
Continuous VWSC training and handholding is required to build capacity for O&M, tariff collection, and water governance.
Coordination across multiple agencies (ITDA, RWS, PR&RD, VWSCs & DWMA) and evolving JJM guidelines increases administrative complexity.
Entrustment, tendering and monitoring processes face delays due to scattered geography, low contractor interest and logistical constraints
Operational
Steep hilly terrain and forest interiors make many habitations accessible only by foot limiting material movement.
Scattered, low-density tribal settlements increase pipeline length and reduce system viability.
Weak and variable groundwater availability with dependence on seasonal springs and surface flows.

## Slide 4
Used lightweight materials & community labour mobilisation to overcome inaccessibility in foot-path-only terrain.
Best Practice (1) Gravity Fed Spring Water Systems (ASR Hill Terrain)
Adopted gravity-fed spring systems to serve remote hilltop habitations with zero power dependence
Designed decentralized micro-schemes for scattered, low-density tribal settlements to ensure feasibility and coverage
Why Needed: Remote hilltop habitations, weak groundwater, foot path only access.
Technical Features:
Perennial spring sources yielding 0.5 -1 LPS
HDPE pipelines (50–90 mm) aligned on natural contours
5-60 KL ELSRs with roughing + sand filtration
Community & VWSC Role:
Spring protection, pipeline alignment support, daily monitoring
VWSC handles valve operation & minor repairs
Impact:
100% FHTCs in remote tribal villages
Zero power cost, highly sustainable.
Area of Implementation: G. Madugula block habitations are Neredubanda, Chinaporlu, Seethabanda.
Layout map of Neredubanda habitation

## Slide 5
Best Practice – (2) Solar Dual Pump Systems (Off-Grid Tribal Villages)
Adopted gravity-fed spring systems to serve remote hilltop habitations with zero power dependence
Designed decentralized micro-schemes for scattered, low-density tribal settlements to ensure feasibility and coverage
Why Needed: No electricity, unreliable power, pump downtime in interior mandals.
Technical Features:
1–2 HP solar pumps + 2–3 kW panels.
8,000–12,000 L/day discharge output.
5–10 KL storage tanks supplying 55 LPCD.
Community & VWSC Role:
Youth clean solar panels & protect fencing
VWSC collects small O&M contribution
Impact:
24×7 water supply with zero electricity bills
No diesel, no pump failure, higher reliability.
Where Implemented: Bangarammapet
RWS Team explaining community about the use of the Solar energy for the water supply
Solar Based water collection point

## Slide 6
Used lightweight materials & community labour mobilisation to overcome inaccessibility in foot-path-only terrain.
Best Practice (3) - Community Engagement, FTK Monitoring & Jala Devalayam
Adopted gravity-fed spring systems to serve remote hilltop habitations with zero power dependence
Why Needed: Low water-quality awareness, reservoir contamination risk, weak ownership.
Technical Features:
Bi-weekly FTK testing (pH, turbidity, chlorine, nitrate, iron)
Jala Devalayam: compound wall, plantation, IEC murals and walkway work as a common point for the community
Community & VWSC Role:
VWSC digitizes FTK records
teachers support IECI
Impact:
Higher water safety awareness, fewer contamination incidents.
Reservoirs protected & community pride increased
Best Fit: All villages with GLSRs, especially where source quality varies Where Implemented: 5 habs of Ananatagiri
Water Source made as worshiping place with all amendments as the community culture follows
Head Works made as a park with all amenities
for the community to own

## Slide 7
Used lightweight materials & community labour mobilisation to overcome inaccessibility in foot-path-only terrain.
Best Practice (4) - VWSC Strengthening & Institutional Capacity
Adopted gravity-fed spring systems to serve remote hilltop habitations with zero power dependence
Why Needed: Weak local O&M capacity, low tariff collection, limited technical skills.
Technical Features / Capacity Actions:
VWSCs formalized with 11–15 members, 50% women
Training topic are 1. Valve operation 2. Meter reading 3.Leak detection 4.Chlorination.
Monthly O&M registers and other financial books maintenance.
Support from VJNNS (Narsipatnam):
Hands on plumbing demos, pump repair basics, chlorine application
Field-based training & IEC tools in local language
Impact:
VWSCs operate schemes independently
Faster repairs, improved O&M discipline and tariff recovery
District Coverage: All mandals under DWSM + VJNNS support cycle.
VWSC Training on O&M and tariff recovery
VJNNS workshop in Narsipatnam

## Slide 8
Best Practice (5) - Multi Village Scheme for sustainable rural water supply
Designed decentralized micro-schemes for scattered, low-density tribal settlements to ensure feasibility and coverage
Why It Works in ASR District :
Ideal for hilly terrain with scattered settlements and unreliable groundwater.
Reduces infrastructure duplication and ensures uniform service levels across connected villages.
Maintains stable water supply even during peak summer reducing tanker dependency
Core Features of ASR’s MVS Model :
Uses perennial springs with 2–5 LPS dependable discharge as main sources for clusters of habitations.
Gravity-fed networks minimize energy requirements, pumping and O&M costs.
20–50 KL GLSRs placed at strategic elevations supply multiple villages efficiently.
Standardized filtration improves safety: roughing filters + slow sand filters + chlorine dosing.
Where Implemented :
Araku Valley–Sunkarammetta Corridor
Ananthagiri High-Yield Spring Cluster
G. Madugula Spring Pocket Villages
Community & VWSC Integration :
VWSCs manage valve operations, preventive maintenance and source protection.
Youth and community members support spring-shed protection, fencing, and water quality monitoring.
Layout map of Araku Valley Sunkarammetta Corridor
Schematic diagram of Araku Valley –sunkarammetta Corridor

## Slide 9
Expand Multi-Village Schemes & Water Grid Model :
Need: Many tribal habitations have unreliable springs or seasonal surface sources.
Proposal: Develop larger MVS corridors and a district-level Water Grid to ensure year-round security.
Shift from Unit-Based Projects to Population-Based Projects :
Need: Current unit-based estimations do not match the terrain realities of low-density tribal villages.
Proposal: Adopt population-based and habitation-cluster models to provide technically viable schemes in hilly regions.
Budget Support for District IEC & Training :
Need: Remote tribal villages require strong IEC, continuous FTK training, VWSC handholding and community mobilisation.
Proposal: Provide dedicated budget for district-level IEC vans, cluster workshops, Jala Devalayam expansion, and VWSC capacity-building.
ASR District requests sustained technical & financial support for resilient, community-led drinking
water systems in challenging tribal terrain
Strategic Way Forward & Support Required for ASR District

## Slide 10
Ensuring Safe Drinking Water for Every Rural Household
Thank You
Collector & District Magistrate,
Alluri Sitharama Raju District
Andhra Pradesh