## Slide 1
PUBLIC HEALTH ENGINEERING DEPARTMENT HARYANA
Welcomes You

## Slide 3: WHAT IS RANNEYWELL
History of Ranneywell :
Ranney well were invented by Leo Ranney a Petroleum Engineer in Texas Oil field city of St. Helens, during the year 1920, his idea was to gather larger quantity of oil.
The 1stRanney well of water supply was dug in London, England 1933.

## Slide 4: Ranney Wells in India – History, Locations and Benefits
1. Introduction A Ranney well, also known as a radial collector well, is a groundwater abstraction system constructed in river flood plains. It collects naturally filtered river water through horizontal laterals laid in sandy aquifers. In India, Ranney wells are considered a strategic source for bulk and reliable urban water supply.
2. Timeline of Ranney Wells in India
1970–1980 (Introduction Phase) Ranney well technology was introduced in India during the 1970s due to rapid urbanization, increasing pollution in surface water sources, and the need for dependable bulk water supply.

## Slide 5
3. Locations of Ranney Wells in India
Yamuna Flood Plain: Delhi (Palla area), Sonipat, Panipat, Yamunanagar, Faridabad–Palwal belt.
Ganga Flood Plain: Kanpur, Prayagraj, Varanasi, Patna, Bhagalpur.
Other River Basins: Godavari (Nashik, Nanded), Narmada (Jabalpur, Bharuch).
4. Typical Ranney Well Configuration
Collector well diameter: 6 – 9 mtr. Depth: 25 - 40 mtr. 10 no. Laterals inserted in one layer .
30 mtr. Approximately Screen Pipe inserted in 1 no. lateral.
Discharge: 8–12 MLD (site dependent)

## Slide 9: 5. Benefits of Ranney Wells
• Natural filtration through sand and gravel • Low turbidity and reduced bacterial contamination • Protection from direct river pollution • High and stable yield even in summer • Better chemical quality than tubewells • Lower long-term Operation &Maintenance cost • Sustainable source with continuous river recharge
Greater screen length, screen surface, and capacity per well.
Concentration of operation requires minimal land acquisition.
Relatively low draw- down and use of efficient, high capacity pumps results in long term savings in energy consumption.
Less road construction, electrical and mechanical controls, and associated pipe line as compared to battery of tubewells.
One Ranney Well of 10.0 Mld (Million Litres per Day)capacity is equivalent to 30-40 Nos. tubewells in the same area.

## Slide 10: DISTRICT PALWAL
Geographical Area:- 1,368 sq km
Altitude:- 195 Mtr (639 ft)
Latitude:- 28.40 deg N
Longitude:- 76.59 deg E
Population (Census 2011):- 10,40,493
Average Temperature:- 34.4 deg C
Average Annual Rainfall:- 454 mm
Number of Villages:- 263
Number of blocks:- 6 Nos. (Palwal,Hodal, Hathin, Hassanpur, Prithla,Badoli)
Profile:- Palwal became the 21st district of Haryana State on 15 August 2008 Palwal city as its headquarters.
Geography & Climate:- Palwal is located in the southern part of Haryana . It shares a geographical boundary with Mewat, Aligarh, Gurgaon, Faridabad and Delhi.

## Slide 11
Existing Drinking Water position in Project Area
Earlier drinking water in the 84 villages of project area is supplied @ 55 LPCD (Litre per capita per day) by installing 136 No. tube wells near by villages in which the water Quality is deteriorating and quantity is reducing day by day.
84 villages covers:-
29 villages of Prithla block
38 villages of Palwal block
17 villages of Ballabgarh Block

## Slide 12: Necessity of Project
Name of Project :-Augmentation Drinking water supply scheme in quality affected 84 No. Villages of Prithla & Palwal Block of Distt. Palwal & Ballabgarh Block of Distt. Faridabad from Yamuna flood plain by construction of Ranneywell and deep Tubewell in village Mohna.
Estimated Cost Rs.184.30.00 Crore
“Initially, water supply was being operated through tubewells. Over time, issues related to poor water quality, including high turbidity, iron content, and bacteriological concerns, were observed. In order to overcome these issues and to provide safe, reliable, and sustainable drinking water, the department adopted Ranney (Radial Collector) Well technology in the Yamuna flood plain area.”
Presently drinking water in the 84 villages of project area is supplied @ 70 LPCD (Litre per capita per day) by installing of 2 No. Rannewells and 2 No. tube wells nearby Yamuna flood plains.
The water abstracted from the Ranney Wells is conveyed to 2 Nos. Main Boosting Stations (MBS) and further distributed through 7 Nos. Intermediate Boosting Stations (IBS), from where potable water supply is ensured to Villages of Prithla & Palwal Block of Distt. Palwal & Ballabgarh Block of Distt. Faridabad .”

## Slide 13
This project provides water supply to following villages with population of 346975 (Designed for the year 2031) :-
29 villages of Prithla block
38 villages of Palwal block
17 villages of Ballabgarh Block
Further water is supplied to following villages by IBS :-
IBS Mandkol – 9 no. villages
IBS Dudhola – 14 no. villages
IBS Ratipur – 11 no. villages
IBS Dhatir – 14 no. villages
IBS Kairaka – 13 no. villages
IBS Prithla – 6 no. villages
IBS Bhanakpur – 17 no. villages

## Slide 14
“After shifting to Ranney Wells, water quality and supply reliability have improved and public complaints related to drinking water have reduced significantly.”

## Slide 15
Flow Chart

## Slide 16
CONSTRUCTION OF 2 NOS. RANNEY WELLS (20 mld), Tubewells (2 Nos.)
Main Boosting Station Mohna (UGT 6100 KL)
MBS Dudhola (UGT 4500 KL)
PROJECT AT A GLANCE
600mm i/d, (D.I. Pipe)1200 m
800mm I/d (Pre stressed Concrete Cylinder Pipe) PCCP Length:- 13450 M.
IBS Mandkol (750 KL)
7 nos. villages
2 nos. villages
IBS Dudhola (4500KL)
14 No. villages
IBS Dhatir (800 KL)
IBS Kairaka (500 KL)
IBS Ratipur (850 KL)
IBS Bhanakpur (1200 KL)
IBS Prithla (500 KL)
14 No. villages
13 No. villages
11 No. villages
17 No. villages
6 No. villages
700 mm i/d (Pre stressed Concrete Cylinder Pipe) PCCP Length :-9500M

## Slide 17
Sr. No. | Characteristics |  | Results of |  |  | 
 |  | Max. Permissible limit as per CPHEEO Manual | Ranneywell No.1 | Ranneywell No.2 | Remarks | 
 | Turbidity (NTU) | 0 | 0 | 0 | Potable | 
 | Colour (platinum cobalt scale) | Cl | Cl | Cl | Potable | 
 | Taste and odour | Agreeable | Agreeable | Agreeable | Potable | 
 | pH (Hydrogen Potential) | 6.50-8.50 | 7.59 | 6.74 | Potable | 
 | Total dissolved solids (mg/I) | 2000 | 796 | 253 | Potable | 
 | Total hardness (mg/l) as CaCO3 | 600 | 400 | 200 | Potable | 
 | Chlorides (as Cl) mg/l | 1000 | 360 | 110 | Potable | 
 | Alkanity (mg/ltr.) | 600 | 390 | 340 | Potable | 
 | Sulphates (as SO4) mg/l | 400 | 92 | 43 | Potable | 
 | Fluorides (as F) (mgl/l) | 1.5 | 0.1 | 0.63 | Potable | 
 | Nitrates (as NO3) (mg/l) | 100 | 1.14 | 0.49 | Potable | 
 | Calcium (as Ca) (mg/l) | 200 | 80 | 20 | Potable | 
 | Magnesium (as Mg) (mg/l) | 100 | 48 | 36 | Potable | 
 | Iron (as Fe) (mg/l) | 1.0 | 0.01 | 0.06 | Potable | 
The water quality of existing Ranney Wells (Village Mohna)

## Slide 18: Construction of Ranneywell

## Slide 19
CUTTING EDGE

## Slide 20: CUTTING EDGE INNER SHUTTERING

## Slide 21: CUTTING EDGE STEEL

## Slide 22: CUTTING EDGE CASTING

## Slide 23: CUTTING EDGE AFTER CASTING

## Slide 24
PORT HOLES 1st LAYER

## Slide 25
PORT HOLES 2ND LAYER

## Slide 26: STEINING WALL CASTING

## Slide 27: PLATEFORM STEEL

## Slide 28: PLATEFORM STEEL AND CASTING

## Slide 29: PUMP CHAMBER

## Slide 30: PUSHING OF STAINER PIPE

## Slide 31: SAND VALVE AND STAINER PIPE

## Slide 32: EXTRACTION OF DESANDING

## Slide 33: DE-SILTING

## Slide 34: PLATEFORM FOR PUMPING MACHINERY

## Slide 35: FOUNDATION OF PUMPING MACHINERY

## Slide 36: TOP BEAM CASTING

## Slide 37: SHUTTERING OF ROOF

## Slide 38: ROOF STEEL

## Slide 39: PUMP CHAMBER

## Slide 40: PUMPING MACHINERY

## Slide 41: PUMP CHAMBER

## Slide 42: THANK YOU